## Slide 1
I- Definition
A reinforced concrete element is subjected to axial actions when it is loaded by two directly opposing forces, applied at the center of its end surfaces, tending either to elongate or shorten it.
When this axial force is compressive (N-), the element is said to be under simple compression.
N : Normal force
T : Shear force
M : Bending moment
Element Subjected to Compression
university center of Mila
Course : Reinforced concrete
Chapter 04: Design of Sections Under Axial Loads - Simple Compression

## Slide 2
II.Calculation Assumptions
The eccentricity of the normal force is small.
Imperfection of straightness is less than max(1cm; l₀/500), where l₀ is the free length.
Slenderness ratio less than 70.
For a column under 'axial compression', the center of gravity of concrete coincides with that of reinforcement.
BAEL rules impose no SLS conditions for columns in axial compression. Hence, design and reinforcement determination must be performed at ULS only.
With concrete fully compressed, the strain diagram passes through Pivot C (εbc= 2‰).
No relative slip between steel and concrete (εbc = εsc = 2 ‰).
III. Basic Action Combination:
In most common cases, the only action combination to consider is:

## Slide 3
IV Buckling Length and Slenderness of a Column
IV.1. Buckling Length (Lf): Under compression, columns may buckle. Calculations must use a fictive length (Lf), dependent on end conditions, instead of the real length (L₀).
The buckling length 𝐿𝑓L f​ depends on the type of connection at the ends of the considered element. Generally speaking:
A-Case of isolated columns:
K: Relationship between free length L₀ and buckling length Lf.
B-Case of buildings:
Free length L₀ measured:
- between top faces of consecutive floors.
- between foundation top face and first floor top face.

## Slide 4
b. Case of a typical floor – Inertias: If the inertias of the beams are greater than the inertia of the column:Ipoutre 1 ≥ Ipoteau et Ipoutre 2 ≥ Ipoteau )
Case of a column on foundation:
In other cases:
IV.2. Slenderness: Slenderness is denoted by the symbol λ, and it is defined as the ratio of the buckling length 𝐿𝑓​ to the minimum radius of gyration 𝑖:
:With : where
–​: : is the minimum moment of inertia of the column's section – B: is the section of the column.
Example :
Poutre1
Poutre2
semelle
poteau
poteau
Section Type | Section Area (B) | (Iₘᵢₙ) Minimum Moment of Inertia | (i) Radius of gyration | (λ) Slenderness
Rectangle (a × b) |  |  |  | 
Circle (Diameter D) |  |  |  | 
Section Type | Section Area (B) | (Iₘᵢₙ) Minimum Moment of Inertia | (i) Radius of gyration | (λ) Slenderness
Rectangle (a × b) |  |  |  | 
Circle (Diameter D) |  |  |  | 

## Slide 5
V. Calculation at the Ultimate Limit State of Resistance: According to the resistance condition, the acting axial force 𝑁𝑢 u​ must be less than or equal to the ultimate resistanceNulimite :
If A and 𝐵 are known, we calculate 𝑁𝑢.𝑅 In pure compression, the strain diagram passes through the pivot point C where:
The theoretical limit axial force is:
Where: and
V.1 Calculation at the Limit State of Buckling Stability: For greater safety (to compensate for construction defects), the design code (B.A.E.L) reduces the resistance by a coefficient α, and a reduced concrete section 𝐵𝑟 is used instead of the total section B, to account for sensitivity to construction imperfections. The reduced section 𝐵𝑟 is:
For rectangular sections (a×b):
For circular sections:
The previous function is multiplied by a reduction coefficient (α) to account for the buckling effect, resulting in the ultimate axial force

## Slide 6
A: is the compressed steel section considered in the calculation, and = 1,5 ; = 1,15.
α :is a coefficient depending on the mechanical slenderness λ.
If more than half of the loads are applied at j <90 jours:
α will be divided by :1,10
- If more than half of the loads are applied before 28 days: α will be divided by 1.20 and fcj​ is used instead of fc28
V.2. Determination of Reinforcement: In theory, concrete resists compression well. Therefore, reinforcement is not necessary. However, in practice, in most cases, the loads are not centered (lack of symmetry, construction defects, etc.). For this reason, reinforcement is added.
V.2.1 – Longitudinal Reinforcement:
Calculation of the theoretical section:
Minimum reinforcement ratio: : The following rules must be observed:
- An insufficiently reinforced element is fragile.
An overly reinforced element is impractical to construct properly.
λ≤ 50
50<λ ≤ 70
α

## Slide 7
V.2.1 – Longitudinal Reinforcement:B.A.E.L requires:
P : perimeter of the column in meters. The result is given in cm². B: concrete cross-sectional area
The RPA minimal section requires:
c. Pourcentage d’armature maximum:B.A.E.L exige :
RPA exige: 4% in the regular zone
8% in the overlap (splice) zone
Therefore, the final section to be adopted is:
d. L’espacement entre les armatures longitudinales :The longitudinal reinforcements are distributed within the section near the walls in such a way as to best ensure the flexural strength of the member in the most unfavorable directions. In particular, for a member with a rectangular section, the maximum distance e between two adjacent bars on the same face must not exceed:
λ > 35
R.P.A exige : e< 20cm en zone I et IIa
e< 15cm en zone IIb et III
e. Lap splice length:
The lap splice length 𝑙𝑟​ shall be at least equal to:

## Slide 8
Note: For longitudinal reinforcement, we have three cases:
If ⇒ Use the calculated As.
If or < 0 ⇒ Use the minimum As.
If ⇒ Increase the concrete section B and recalculate As.
V.2.2 – Transverse Reinforcement:These reinforcements mainly serve to hold the longitudinal reinforcement in place. They therefore prevent its buckling.
Diameter:The diameter of the transverse reinforcement must be at least equal to one-third of the diameter of the longitudinal reinforcement (∅𝑙​ ) that they hold in place.
b. Spacing between two stirrups: (St)
In the overlap or nodal zone:B.A.E.L require:
a: the smallest dimension of the member.
RPA require :
In the regular zone:: B.A.E.L requires at least three layers of
transverse reinforcement.
RPA require :

## Slide 9
In the nodal zone, stirrups and ties must be closed using hooks with a straight length of at least 10Øt.
C. Concrete Cover (Encasement C):
C ≥ 3 cm: for superstructures and structures exposed to climatic effects.
C ≥ 5 cm: for structures exposed to aggressive actions (soils, coastal areas, etc.)
V.2.3. Constructive Arrangement:
Reinforcement must be distributed along the walls.
Polygonal sections: at least one bar at each corner. Circular sections: at least 6 bars evenly distributed.